## Slide 1
DISCOVER . LEARN . EMPOWER
INSTITUTE : UIE
DEPARTMENT : CSE
Bachelor of Engineering (Computer Science & Engineering)
WEB AND MOBILE SECURITY (Professional Elective-I)
(20CST/IT-333)
TOPIC OF PRESENTATION:
SIM/UICC Security

## Slide 2: Lecture Objectives
In this lecture, we will discuss:
SIM/UICC Security

## Slide 3: UICC
UICC (Universal Integrated Circuit Card) is the hardware used in mobile devices that contains SIM and/or USIM applications enabling access to GSM, UMTS/3G and LTE networks.
The Universal Integrated Circuit Card (UICC) does a lot more than just the Subscriber Identity Module (SIM). In fact, it runs the SIM application whilst also storing various pieces of information such as the user's contacts list, enabling the use of mobile data and managing data roaming across multiple carriers.
Embedded SIM is a UICC that supports “over the air” provisioning of an initial operator subscription and the subsequent change of subscription from one operator to another in accordance with the GSMA Embedded SIM specification. Use of the GSMA Embedded SIM Specification simplifies industrial and logistic processes for the distribution of M2M equipment.

## Slide 4: SIM
A big differentiator and advantage of the UICC over the SIM is that it can have multiple applications stored on it because of its inherent processing power and larger storage capacity. The SIM card, on the other hand, is simply a storage device.
One of the more important applications in the UICC is USIM (Universal SIM), which identifies the user and the device to the wireless service provider when using standards such as UMTS, HSPA and LTE. Other applications include CSIM (CDMA SIM) for enabling access to CDMA networks and ISIM (IP Multimedia Subsystem SIM) for securing access to multimedia services and non-telecom-related applications such as wireless and automatic payment

## Slide 5: Vulnerabilities/ATTACK
1. Simjacker
In September 2019, security researchers at AdaptiveMobile Security announced they had discovered a new security vulnerability they called Simjacker.
This complex attack carries out SIM card hacking by sending a piece of spyware-like code to a target device using an SMS message.
If a user opens the message, hackers can use the code to spy on their calls and messages—and even track their location.

## Slide 6: The Top Three Simjacker Exploits
More than 1 billion mobile subscribers worldwide are potentially exposed to Simjacker attacks, and the results could be devastating. Simjacker can be used for:
Location tracking. A hacker can use Simjacker to trace a victim’s location and movements without the victim’s knowledge. The hacker sends an SMS message that instructs the SIM card to request the location. The hacker’s phone then receives a code showing the local cell ID of the victim’s phone, enabling the hacker to determine precisely where the cell ID is currently located. The victim’s phone shows no indication that it is being hacked.
Call fraud. Simjacker can also be used along with fraudulent practices to steal money and valuable data from the victim. In this exploit, the hacker’s SMS code instructs the victim’s phone to place a call. The victim’s phone displays a notification text, asking the user to perform an innocuous action, such as tapping OK to continue. When the victim taps OK, the victim’s phone calls the hacker’s phone. In this way, the victim can be tricked into calling an expensive fee-based number.
Browser exploit. In potentially the most damaging exploit, a hacker’s SMS message can instruct the victim’s phone to open a website that contains malware. The hacker can then use social engineering to trick the victim into downloading the malware, or the malware could download automatically.

## Slide 7: 2. SIM card swapping
Another SIM card security issue you may have heard of is SIM card swapping. Hackers used a variation of this technique to take over Twitter CEO Jack Dorsey's personal Twitter account in August 2019. This event raised awareness of how these attacks can be destructive. The technique uses trickery and social engineering, rather than technical vulnerabilities.
A SIM swap attack (also known as SIM porting or SIM hijacking) is where an attacker tricks a mobile phone service provider into transferring a customer’s phone number from the customer’s SIM card, to the attacker’s SIM card.
To perform a SIM card hacking through a SIM card swap, a hacker will first call up your phone provider. They'll pretend to be you and ask for a replacement SIM card. They'll say they want to upgrade to a new device and, therefore, need a new SIM. If they are successful, the phone provider will send them the SIM.
Once the attacker has the target’s mobile phone number transferred to their SIM card, they can then access the target’s SMS messages or voice mails, all without the target knowing. There is a significant risk to those who are targeted because the attacker can use their access to the target’s number to perform sensitive tasks – like changing passwords and authorising financial transactions.
https://www.seeclop.ch/2021/12/21/what-is-simjacking-heres-how-the-mobile-phone-sim-card-scam-works/

## Slide 8: 3. SIM Cloning
In a SIM clone attack, the hacker first gains physical access to your SIM card and then creates a copy of the original. Naturally, for copying your SIM card, the hacker will first take out your SIM from the smartphone.
Attackers use smart card copying software to create a copy of the real SIM card, thereby getting access to the victim’s international mobile subscriber identity (IMSI) and master encryption key.
In the process, the information is burnt onto the SIM card. Yes, physical access to SIM is a must here. That SIM card has to be placed into a card reader from where the data will be copied. In another scenario, SIM cards can be hacked remotely using over-the-air (OTA) communication to breach the encryption protecting the updates sent to the SIM via SMS.
Next, the attacker reaches out to the victim via phone or SMS asks to restart the phone within a given time. Once the victim’s phone gets off, the attacker starts its phone before the victim does. The activity initiates a successful clone followed by an account takeover. But, the hack is completed only after the victim restarts their phone

## Slide 9: How to Keep Your SIM Card Safe
1. Protect Against Socially Engineered Attacks
2. Set a SIM Card Lock
3. Other Security Tips
As always, you should use strong and individually generated passwords. Don't reuse old passwords or use the same password on multiple accounts.
Also, make sure your answers to password recovery questions aren't publicly available—such as your mother's maiden name.
https://www.makeuseof.com/tag/ways-sim-card-hacked/#:~:text=Set%20a%20SIM%20Card%20Lock,they%20need%20the%20PIN%20code.

## Slide 10: Security practices
Put a PIN or password to unlock the SIM card.
Do not share the PIN with absolutely no one.
Keep the PIN and PUK number stored in a safe place.
Use a PIN or key to unlock the SIM card.
Encrypt our data.
NEVER store sensitive information on your cell phone.
Be very careful with the use of bank accounts on the cell phone.
Use a VPN to browse from mobile or any other device.
Do not open attachments that arrive in the mail or any messaging tool if you do not know the sender.
Do not share personal information on the Internet.
Install an antivirus or security tool on your cell phone.
Do not link your bank account to your phone number.
https://gesditel.es/en/sim-card-hacker/

## Slide 11: References:
Books:
Hacking Exposed Mobile: Security Secrets & Solutions 1st Edition, Kindle Edition, by Neil Bergman, Mike Stanfield, Jason Rouse, and Joel Scambray
Hacking Exposed Web Applications, 3rd edition, Joel Scambray, Vincent Liu, Caleb Sima, Released October 2010, Publisher(s): McGraw-Hill
Reference Links:
1. https://justaskthales.com/en/what-uicc-and-how-it-different-sim-card/
3. https://www.makeuseof.com/tag/ways-sim-card-hacked/#:~:text=Set%20a%20SIM%20Card%20Lock,they%20need%20the%20PIN%20code.
Relevant Videos:
https://www.bluetooth.com/learn-about-bluetooth/key-attributes/bluetooth-security/
https://www.thalesgroup.com/en/markets/digital-identity-and-security/technology/sim
https://blog.3g4g.co.uk/search/label/UICC

## Slide 12
THANK YOU